## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 3 Transport Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Slide 1 - Chapter 3 Transport Layer
Book reference (Kurose & Ross, Chapter 3, p. 227): short quote: "TCP is said to be connection-oriented".
Use this slide to connect last week's RDT principles to TCP. TCP provides reliable, ordered, connection-oriented byte-stream service in the real Internet, but it builds that service on top of unreliable IP datagram delivery.
Group the roadmap under four TCP themes: segment structure explains which fields are carried, reliable data transfer explains sequence/ACK/timer logic, flow control protects the receiver buffer, and connection management explains setup and teardown handshakes.
Visible slide keywords: Computer Networking: A Top-Down Approach, 8, th, edition, Jim Kurose, Keith Ross, Pearson, 2020, Chapter 3, Transport Layer, A note on the use of these PowerPoint slides:, We’, re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a, lot, of work on our part. In return for use, we only ask the following:, If you use these slides (e.g., in a class) that you mention their source (after all, we’, d like people to use our book!), If you post any slides on a www site, that you note that they are adap.
Quick question: does TCP inherit reliability from the network layer, or does it create reliability at the endpoints? Expected answer: it creates reliability at the endpoints.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 2: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control
Notes: Slide 2 - Principles of reliable data transfer
Book reference (Kurose & Ross, Chapter 3, p. 227): short quote: "TCP is said to be connection-oriented".
Use this slide to connect last week's RDT principles to TCP. TCP provides reliable, ordered, connection-oriented byte-stream service in the real Internet, but it builds that service on top of unreliable IP datagram delivery.
Group the roadmap under four TCP themes: segment structure explains which fields are carried, reliable data transfer explains sequence/ACK/timer logic, flow control protects the receiver buffer, and connection management explains setup and teardown handshakes.
Visible slide keywords: Chapter 3: roadmap, Transport-layer services, Multiplexing and demultiplexing, Connectionless transport: UDP, Principles of reliable data transfer, Connection-oriented transport: TCP, segment structure, reliable data transfer, flow control, connection management, Principles of congestion control, TCP congestion control, Transport Layer: 3-, 2.
Quick question: does TCP inherit reliability from the network layer, or does it create reliability at the endpoints? Expected answer: it creates reliability at the endpoints.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 3: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Slide 3 - TCP: overview
Book reference (Kurose & Ross, Chapter 3, p. 227): short quote: "A TCP connection provides a full-duplex service".
Treat each TCP overview bullet as a design decision. Point-to-point means two endpoints; full duplex means data can flow both ways in the same connection; reliable in-order byte stream means the application receives the same ordered bytes that were sent.
Spend extra time on no message boundaries. TCP sees application data as a byte stream, not as separate messages. Therefore, the application protocol must define its own framing, length fields, or delimiters.
Visible slide keywords: TCP: overview, RFCs: 793,1122, 2018, 5681, 7323, cumulative ACKs, pipelining:, TCP congestion and flow control set window size, connection-oriented:, handshaking (exchange of control messages) initializes sender, receiver state before data exchange, flow controlled:, sender will not overwhelm receiver, point-to-point, :, one sender, one receiver, reliable, in-order, byte steam:, no “, message boundaries", full duplex data:, bi-directional data flow in same connection, MSS: maximum segment size, Transport Layer: 3-, 3.
Example: if an application performs two separate writes to TCP, must the receiver read them as two separate messages? No, the receiver reads a byte stream.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 4: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification
Notes: Slide 4 - TCP segment structure
Book reference (Kurose & Ross, Chapter 3, p. 230): short quote: "header fields and a data field".
Group the TCP segment fields by function. Ports support demultiplexing; sequence and ACK numbers support reliable transfer; receive window supports flow control; checksum supports error detection; SYN, FIN, and RST support connection management; C and E bits relate to congestion notification.
Students should not memorize the header as a flat table. Every field is evidence of a TCP service. TCP has a more complex header than UDP because it provides more control and stronger guarantees.
Visible slide keywords: TCP segment structure, source port #, dest, port #, 32 bits, not, used, receive window, flow control:, # bytes receiver willing to accept, sequence number, segment seq #:, counting bytes of data, into, bytestream, (not segments!), application, data, (variable length), data sent by application into TCP socket, A, acknowledgement number, ACK:, seq # of next expected byte; A bit: this is an ACK, options (variable length), TCP, options, head, len, length, (of TCP header), checksum, Internet, checksum, RST, SYN, FIN:, connection management, F, S, R, Urg, data pointer, P, U, C, E, C, E:, congestion notification, Transport Layer: 3-, 4.
Key point: the receive window field tells the sender how many more bytes the receiver is willing to accept.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 5: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
Notes: Slide 5 - TCP sequence numbers, ACKs
Book reference (Kurose & Ross, Chapter 3, p. 232): short quote: "sequence numbers are over the stream of transmitted bytes".
Explain sequence and ACK numbers in terms of bytes. A segment's sequence number is not a segment number; it is the number of the first byte in that segment's data. The ACK number is the next byte expected from the other side.
In the Telnet example, trace the echoed C character step by step. Host A sends data with its own sequence number and includes the byte it expects from B as the ACK. Host B both acknowledges A's byte and sends its own data back. This is a small example of full duplex behavior.
Visible slide keywords: TCP sequence numbers, ACKs, Sequence numbers:, byte stream “, number” of first byte in segment’s data, source port #, dest port #, sequence number, acknowledgement number, checksum, rwnd, urg pointer, outgoing segment from receiver, A, sent, ACKed, sent, not-yet, ACKed, (“, in-flight”), usable, but not, yet sent, not, usable, window size, N, sender sequence number space, source port #, dest port #, sequence number, acknowledgement number, checksum, rwnd, urg pointer, outgoing segment from sender, Acknowledgements, :, seq # of next byte expected from other side, cumulative ACK, Q, :, how receiver handles out-of-order segments, A:, TCP spec doesn, ’t say, - up to implementor, Transport Layer: .
Quick question: what does ACK=43 mean? It means bytes through 42 have been received and byte 43 is expected next.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 6: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: Slide 6 - TCP sequence numbers, ACKs
Book reference (Kurose & Ross, Chapter 3, p. 232): short quote: "sequence numbers are over the stream of transmitted bytes".
Explain sequence and ACK numbers in terms of bytes. A segment's sequence number is not a segment number; it is the number of the first byte in that segment's data. The ACK number is the next byte expected from the other side.
In the Telnet example, trace the echoed C character step by step. Host A sends data with its own sequence number and includes the byte it expects from B as the ACK. Host B both acknowledges A's byte and sends its own data back. This is a small example of full duplex behavior.
Visible slide keywords: TCP sequence numbers, ACKs, host ACKs receipt of echoed, ‘, C, ’, host ACKs receipt of, ‘, C, ’, , echoes, back, ‘, C, ’, simple telnet scenario, Host B, Host A, User types, ‘, C, ’, Seq=42, ACK=79, data =, ‘, C, ’, Seq=79, ACK=43, data =, ‘, C, ’, Seq=43, ACK=80, Transport Layer: 3-, 6.
Quick question: what does ACK=43 mean? It means bytes through 42 have been received and byte 43 is expected next.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 7: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT
Notes: Slide 7 - TCP round trip time, timeout
Book reference (Kurose & Ross, Chapter 3, p. 235): short quote: "estimate of this round-trip time".
For RTT and timeout, explain the core tradeoff: timeout should be longer than RTT, but not too long. If it is too short, TCP performs unnecessary retransmissions; if it is too long, TCP reacts slowly to real loss.
Explain EstimatedRTT as an EWMA. The new SampleRTT influences the estimate, but older measurements are not discarded at once. DevRTT measures variability; TimeoutInterval = EstimatedRTT + 4*DevRTT adds a safety margin.
Visible slide keywords: TCP round trip time, timeout, Q:, how to set TCP timeout value?, longer than RTT, but RTT varies!, too short:, premature timeout, unnecessary retransmissions, too long:, slow reaction to segment loss, Q, :, how to estimate RTT?, SampleRTT:, measured, time from segment transmission until ACK receipt, ignore retransmissions, SampleRTT, will vary, want estimated RTT “, smoother, ”, average several, recent, measurements, not just current, SampleRTT, Transport Layer: 3-, 7.
Key point: TCP normally ignores SampleRTT measurements for retransmitted segments because it becomes ambiguous which transmission the ACK corresponds to.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 8: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: Slide 8 - TCP round trip time, timeout
Book reference (Kurose & Ross, Chapter 3, p. 235): short quote: "estimate of this round-trip time".
For RTT and timeout, explain the core tradeoff: timeout should be longer than RTT, but not too long. If it is too short, TCP performs unnecessary retransmissions; if it is too long, TCP reacts slowly to real loss.
Explain EstimatedRTT as an EWMA. The new SampleRTT influences the estimate, but older measurements are not discarded at once. DevRTT measures variability; TimeoutInterval = EstimatedRTT + 4*DevRTT adds a safety margin.
Visible slide keywords: TCP round trip time, timeout, EstimatedRTT, = (1-, , )*, EstimatedRTT, +, , *, SampleRTT, e, xponential, w, eighted, m, oving, a, verage (EWMA), influence of past sample decreases exponentially fast, typical value:, , =, 0.125, RTT (milliseconds), RTT:, gaia.cs.umass.edu, to, fantasia.eurecom.fr, sampleRTT, EstimatedRTT, time (seconds), Transport Layer: 3-, 8.
Key point: TCP normally ignores SampleRTT measurements for retransmitted segments because it becomes ambiguous which transmission the ACK corresponds to.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 9: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
Notes: Slide 9 - TCP round trip time, timeout
Book reference (Kurose & Ross, Chapter 3, p. 235): short quote: "estimate of this round-trip time".
For RTT and timeout, explain the core tradeoff: timeout should be longer than RTT, but not too long. If it is too short, TCP performs unnecessary retransmissions; if it is too long, TCP reacts slowly to real loss.
Explain EstimatedRTT as an EWMA. The new SampleRTT influences the estimate, but older measurements are not discarded at once. DevRTT measures variability; TimeoutInterval = EstimatedRTT + 4*DevRTT adds a safety margin.
Visible slide keywords: TCP round trip time, timeout, timeout interval:, EstimatedRTT, plus “, safety margin”, large variation in, EstimatedRTT, :, want a larger safety margin, TimeoutInterval, =, EstimatedRTT, + 4*, DevRTT, estimated RTT, “, safety margin, ”, * Check out the online interactive exercises for more examples: h, ttp://, gaia.cs.umass.edu, /, kurose_ross, /interactive/, DevRTT, =, (1-, , )*, DevRTT, +, , *|, SampleRTT-EstimatedRTT, |, (typically,, , = 0.25), DevRTT, : EWMA of, SampleRTT, deviation from, EstimatedRTT, :, Transport Layer: 3-, 9.
Key point: TCP normally ignores SampleRTT measurements for retransmitted segments because it becomes ambiguous which transmission the ACK corresponds to.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 10: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: Slide 10 - TCP Sender
Book reference (Kurose & Ross, Chapter 3, p. 239): short quote: "single retransmission timer".
Read the TCP sender algorithm as event-driven behavior: when data arrives from the application, a segment is created, a sequence number is assigned, and the timer starts if needed. On timeout, the oldest unacknowledged segment is retransmitted. On ACK arrival, SendBase advances.
In the receiver ACK generation table, explain delayed ACK, cumulative ACK, and duplicate ACK behavior. When an out-of-order segment creates a gap, the receiver sends a duplicate ACK for the next byte it still expects.
Visible slide keywords: TCP Sender, (simplified), event: data received from application, create segment with seq #, seq # is byte-stream number of first data byte in segment, start timer if not already running, think of timer as for oldest, unACKed, segment, expiration interval:, TimeOutInterval, event: timeout, retransmit segment that caused timeout, restart timer, event: ACK received, if ACK acknowledges previously, unACKed, segments, update what is known to be, ACKed, start timer if there are still, unACKed, segments, Transport Layer: 3-, 10.
Quick question: does this simplified TCP model use a separate timer for every segment? No; the book describes a single retransmission timer.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 11: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: Slide 11 - TCP Receiver: ACK generation
Book reference (Kurose & Ross, Chapter 3, p. 239): short quote: "single retransmission timer".
Read the TCP sender algorithm as event-driven behavior: when data arrives from the application, a segment is created, a sequence number is assigned, and the timer starts if needed. On timeout, the oldest unacknowledged segment is retransmitted. On ACK arrival, SendBase advances.
In the receiver ACK generation table, explain delayed ACK, cumulative ACK, and duplicate ACK behavior. When an out-of-order segment creates a gap, the receiver sends a duplicate ACK for the next byte it still expects.
Visible slide keywords: TCP Receiver: ACK generation, [RFC 5681], Event at receiver, arrival of in-order segment with, expected seq #. All data up to, expected seq # already, ACKed, arrival of in-order segment with, expected seq #. One other, segment has ACK pending, arrival of out-of-order segment, higher-than-expect seq. # ., Gap detected, arrival of segment that, partially or completely fills gap, TCP receiver action, delayed ACK. Wait up to 500ms, for next segment. If no next segment,, send ACK, immediately send single cumulative, ACK,, ACKing, both in-order segments, immediately send, duplicate ACK, ,, indicating seq. # of next expected byte, immediate send ACK, provided that, segment starts at lower end of ga.
Quick question: does this simplified TCP model use a separate timer for every segment? No; the book describes a single retransmission timer.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 12: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: Slide 12 - TCP: retransmission scenarios
Book reference (Kurose & Ross, Chapter 3, p. 239): short quote: "single retransmission timer".
Use the time diagrams to explain retransmission scenarios. In a lost ACK case, the sender may think data was lost and retransmit after timeout. If a later cumulative ACK acknowledges a further byte, the earlier lost ACK is effectively covered.
For fast retransmit, emphasize the three duplicate ACK idea. The sender does not wait for timeout; repeated ACKs for the same next expected byte strongly suggest that a segment is missing. This improves reaction time after loss.
Visible slide keywords: TCP: retransmission scenarios, lost ACK scenario, Host B, Host A, Seq=92, 8 bytes of data, Seq=92, 8 bytes of data, ACK=100, X, ACK=100, timeout, premature timeout, Host B, Host A, Seq=92, 8, bytes of data, ACK=120, timeout, ACK=100, ACK=120, SendBase, =100, SendBase, =120, SendBase, =120, Seq=92, 8 bytes of data, Seq=100, 20 bytes of data, SendBase, =92, send cumulative, ACK for 120, Transport Layer: 3-, 12.
Key point: a duplicate ACK is not absolute proof, but it is a strong signal that TCP can use for performance.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 13: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: Slide 13 - TCP: retransmission scenarios
Book reference (Kurose & Ross, Chapter 3, p. 239): short quote: "single retransmission timer".
Use the time diagrams to explain retransmission scenarios. In a lost ACK case, the sender may think data was lost and retransmit after timeout. If a later cumulative ACK acknowledges a further byte, the earlier lost ACK is effectively covered.
For fast retransmit, emphasize the three duplicate ACK idea. The sender does not wait for timeout; repeated ACKs for the same next expected byte strongly suggest that a segment is missing. This improves reaction time after loss.
Visible slide keywords: TCP: retransmission scenarios, cumulative ACK covers for earlier lost ACK, Host B, Host A, Seq=92, 8 bytes of data, Seq=120, 15 bytes of data, Seq=100, 20 bytes of data, X, ACK=100, ACK=120, Transport Layer: 3-, 13.
Key point: a duplicate ACK is not absolute proof, but it is a strong signal that TCP can use for performance.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 14: TCP fast retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: Slide 14 - TCP fast retransmit
Book reference (Kurose & Ross, Chapter 3, p. 239): short quote: "single retransmission timer".
Use the time diagrams to explain retransmission scenarios. In a lost ACK case, the sender may think data was lost and retransmit after timeout. If a later cumulative ACK acknowledges a further byte, the earlier lost ACK is effectively covered.
For fast retransmit, emphasize the three duplicate ACK idea. The sender does not wait for timeout; repeated ACKs for the same next expected byte strongly suggest that a segment is missing. This improves reaction time after loss.
Visible slide keywords: TCP fast retransmit, Host B, Host A, timeout, ACK=100, ACK=100, ACK=100, ACK=100, X, Seq=92, 8 bytes of data, Seq=100, 20 bytes of data, Seq=100, 20 bytes of data, Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!, if sender receives 3 additional ACKs for same data, (“, triple duplicate ACKs”),, resend, unACKed, segment with smallest seq #, likely that, unACKed, segment lost, so don’, t wait for timeout, TCP fast retransmit, Transport Layer: 3-, 14.
Key point: a duplicate ACK is not absolute proof, but it is a strong signal that TCP can use for performance.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 15: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control
Notes: Slide 15 - Principles of reliable data transfer
Book reference (Kurose & Ross, Chapter 3, p. 246): short quote: "flow control is thus a speed-matching service".
Use this roadmap slide to mark the transition from reliable transfer to flow control. The problem is no longer only loss in the network; it is also the possibility that the receiving application reads from the buffer too slowly.
Separate the two control ideas: flow control protects the receiver; congestion control protects the network. Both can limit the sender's rate, but for different reasons.
Visible slide keywords: Chapter 3: roadmap, Transport-layer services, Multiplexing and demultiplexing, Connectionless transport: UDP, Principles of reliable data transfer, Connection-oriented transport: TCP, segment structure, reliable data transfer, flow control, connection management, Principles of congestion control, TCP congestion control, Transport Layer: 3-, 15.
Quick question: if the receiver buffer is full, is that necessarily network congestion? No, it may be receiver-side speed mismatch.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 16: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
Notes: Slide 16 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 246): short quote: "flow control is thus a speed-matching service".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, application, process, TCP socket, receiver buffers, TCP, code, IP, code, receiver protocol stack, Q:, What happens if network layer delivers data faster than application layer removes data from socket buffers?, Network layer delivering IP datagram payload into TCP socket buffers, from sender, Application removing data from TCP socket buffers, Transport Layer: 3-, 16.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 17: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
Notes: Slide 17 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 246): short quote: "flow control is thus a speed-matching service".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, application, process, TCP socket, receiver buffers, TCP, code, IP, code, receiver protocol stack, Q:, What happens if network layer delivers data faster than application layer removes data from socket buffers?, Network layer delivering IP datagram payload into TCP socket buffers, from sender, Application removing data from TCP socket buffers, Transport Layer: 3-, 17.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 18: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
from sender
Application removing data from TCP socket buffers
receive window
flow control: # bytes receiver willing to accept
Notes: Slide 18 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 246): short quote: "flow control is thus a speed-matching service".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, application, process, TCP socket, receiver buffers, TCP, code, IP, code, receiver protocol stack, Q:, What happens if network layer delivers data faster than application layer removes data from socket buffers?, from sender, Application removing data from TCP socket buffers, receive window, flow control:, # bytes receiver willing to accept, Transport Layer: 3-, 18.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 19: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control
from sender
Application removing data from TCP socket buffers
Notes: Slide 19 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 246): short quote: "flow control is thus a speed-matching service".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, application, process, TCP socket, receiver buffers, TCP, code, IP, code, receiver protocol stack, Q:, What happens if network layer delivers data faster than application layer removes data from socket buffers?, receiver controls sender, so sender won’, t overflow receiver’s buffer by transmitting too much, too fast, flow control, from sender, Application removing data from TCP socket buffers, Transport Layer: 3-, 19.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 20: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP receiver-side buffering
Notes: Slide 20 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 247): short quote: "variable called the receive window".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, TCP receiver “, advertises” free buffer space in, rwnd, field in TCP header, RcvBuffer, size set via socket options (typical default is 4096 bytes), many operating systems, autoadjust, RcvBuffer, sender limits amount of, unACKed, (“, in-flight”) data to received, rwnd, guarantees receive buffer will not overflow, buffered data, free buffer space, rwnd, RcvBuffer, TCP segment payloads, to application process, TCP receiver-side buffering, Transport Layer: 3-, 20.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 21: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
flow control: # bytes receiver willing to accept
receive window
TCP segment format
Notes: Slide 21 - TCP flow control
Book reference (Kurose & Ross, Chapter 3, p. 247): short quote: "variable called the receive window".
Make the receiver buffer concrete. The network layer delivers data to TCP, TCP places it in the receive buffer, and the application process reads it through the socket. If the application reads slowly, the buffer fills; if the sender continues at the same rate, overflow can occur.
The TCP receiver advertises free buffer space using rwnd. The idea is rwnd = RcvBuffer - (LastByteRcvd - LastByteRead). The sender limits the amount of in-flight data according to that advertised window so the receiver's capacity is not exceeded.
Visible slide keywords: TCP flow control, TCP receiver “, advertises” free buffer space in, rwnd, field in TCP header, RcvBuffer, size set via socket options (typical default is 4096 bytes), many operating systems, autoadjust, RcvBuffer, sender limits amount of, unACKed, (“, in-flight”) data to received, rwnd, guarantees receive buffer will not overflow, flow control:, # bytes receiver willing to accept, receive window, TCP segment format, Transport Layer: 3-, 21.
Key point: rwnd comes from the receiver; the congestion window is about network congestion. Real TCP sending behavior is constrained by both.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 22: TCP connection management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: Slide 22 - TCP connection management
Book reference (Kurose & Ross, Chapter 3, p. 227): short quote: "TCP is said to be connection-oriented".
Begin connection management by explaining why TCP is connection-oriented. Before data starts, both sides confirm that they are willing to communicate and exchange initial sequence-number information.
A handshake is not merely a greeting; it creates state at the endpoints. Routers do not keep TCP connection state. The state belongs to the TCP stacks in the end hosts.
Visible slide keywords: TCP connection management, before exchanging data, sender/receiver “, handshake”:, agree to establish connection (each knowing the other willing to establish connection), agree on connection parameters (e.g., starting seq #s), connection state: ESTAB, connection variables:, seq # client-to-server, server-to-client, rcvBuffer, size, at server,client, application, network, connection state: ESTAB, connection Variables:, seq # client-to-server, server-to-client, rcvBuffer, size, at server,client, application, network, Socket, clientSocket, =, newSocket, (", hostname","port, number");, Socket, connectionSocket, =, welcomeSocket.accept, ();, Transport Layer: 3-, 22.
Quick question: is TCP connection state stored in routers? No, it is stored in end systems.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 23: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: Slide 23 - Agreeing to establish a connection
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
In the two-way handshake scenarios, explain why variable delay, retransmitted messages, and old duplicate requests cause problems. If request and accept were enough, an old delayed message might be interpreted as a new connection.
Treat x in the slides like an initial sequence number. If the server opens state before it knows the client received the server's response, stale or half-open connection problems can appear.
Visible slide keywords: Agreeing to establish a connection, Q:, will 2-way handshake always work in network?, variable delays, retransmitted messages (e.g., req_conn, (x)) due to message loss, message reordering, c, an’, t, “see” other side, 2-way handshake:, Let’, s talk, OK, ESTAB, ESTAB, choose x, req_conn(x), ESTAB, ESTAB, acc_conn(x), Transport Layer: 3-, 23.
Key point: the three-way handshake lets both sides verify willingness to communicate and sequence-number information.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 24: 2-way handshake scenarios
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!
Notes: Slide 24 - 2-way handshake scenarios
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
In the two-way handshake scenarios, explain why variable delay, retransmitted messages, and old duplicate requests cause problems. If request and accept were enough, an old delayed message might be interpreted as a new connection.
Treat x in the slides like an initial sequence number. If the server opens state before it knows the client received the server's response, stale or half-open connection problems can appear.
Visible slide keywords: 2-way handshake scenarios, connection, x completes, choose x, req_conn(x), ESTAB, ESTAB, acc_conn(x), data(x+1), accept, data(x+1), ACK(x+1), No problem!, Transport Layer: 3-, 24.
Key point: the three-way handshake lets both sides verify willingness to communicate and sequence-number information.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 25: 2-way handshake scenarios
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)
Notes: Slide 25 - 2-way handshake scenarios
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
In the two-way handshake scenarios, explain why variable delay, retransmitted messages, and old duplicate requests cause problems. If request and accept were enough, an old delayed message might be interpreted as a new connection.
Treat x in the slides like an initial sequence number. If the server opens state before it knows the client received the server's response, stale or half-open connection problems can appear.
Visible slide keywords: 2-way handshake scenarios, ESTAB, retransmit, req_conn(x), req_conn(x), client terminates, server, forgets x, connection, x completes, choose x, req_conn(x), ESTAB, ESTAB, acc_conn, (x), acc_conn, (x), Problem: half open connection! (no client), Transport Layer: 3-, 25.
Key point: the three-way handshake lets both sides verify willingness to communicate and sequence-number information.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 26: 2-way handshake scenarios
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
Problem: dup data
accepted!
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)
Notes: Slide 26 - 2-way handshake scenarios
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
In the two-way handshake scenarios, explain why variable delay, retransmitted messages, and old duplicate requests cause problems. If request and accept were enough, an old delayed message might be interpreted as a new connection.
Treat x in the slides like an initial sequence number. If the server opens state before it knows the client received the server's response, stale or half-open connection problems can appear.
Visible slide keywords: 2-way handshake scenarios, client terminates, ESTAB, choose x, req_conn(x), ESTAB, acc_conn(x), data(x+1), accept, data(x+1), connection, x completes, server, forgets x, Problem: dup data, accepted!, data(x+1), retransmit, data(x+1), accept, data(x+1), retransmit, req_conn(x), ESTAB, req_conn, (x).
Key point: the three-way handshake lets both sides verify willingness to communicate and sequence-number information.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 27: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
LISTEN
Server state
LISTEN
clientSocket = socket(AF_INET, SOCK_STREAM)
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
connectionSocket, addr = serverSocket.accept()
clientSocket.connect((serverName,serverPort))
Notes: Slide 27 - TCP 3-way handshake
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
State the TCP three-way handshake clearly: the client sends SYN and chooses x; the server sends SYNACK, acknowledges x+1, and chooses y; the client sends ACK and acknowledges y+1. After this, data transfer begins over the established connection.
Mention that SYN and FIN consume sequence-number space. Students should see ACKnum=x+1 and ACKnum=y+1 not as arbitrary increments but as acknowledgments of the other side's SYN.
Visible slide keywords: TCP 3-way handshake, SYNbit=1, Seq=x, choose init seq num, x, send TCP SYN msg, ESTAB, SYNbit=1, Seq=y, ACKbit=1; ACKnum=x+1, choose init seq num, y, send TCP SYNACK, msg, acking SYN, ACKbit=1, ACKnum=y+1, received SYNACK(x), indicates server is live;, send ACK for SYNACK;, this segment may contain, client-to-server data, received ACK(y), indicates client is live, SYNSENT, ESTAB, SYN RCVD, C, lient, state, LISTEN, S, erver, state, LISTEN, clientSocket, = socket(AF_INET, SOCK_STREAM), serverSocket, = socket(AF_INET,SOCK_STREAM), serverSocket.bind, ((‘’,, serverPort, )), serverSocket.listen, (1), connectionSocket, ,, addr, =, serverSocket.accept, (), clientSocket.connect, ((, serverName,server.
Quick question: why is the third message needed? So the server knows that its own SYN was received by the client.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 28: A human 3-way handshake protocol
1. On belay?
2. Belay on.
3. Climbing.
Notes: Slide 28 - A human 3-way handshake protocol
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
Connect the human handshake analogy to the technical idea: "On belay?" is the request, "Belay on" is acceptance and readiness, and "Climbing" confirms that the acceptance was heard.
Also state the limit of the analogy: TCP messages carry sequence and ACK numbers. Still, the goal is the same: before a critical action begins, both parties must share the same state.
Visible slide keywords: A human 3-way handshake protocol, 1. On belay?, 2. Belay on., 3. Climbing., Transport Layer: 3-, 28.
Key point: reliable protocol design is not only about sending a message; it is also about knowing that the message was received.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 29: Closing a TCP connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
Notes: Slide 29 - Closing a TCP connection
Book reference (Kurose & Ross, Chapter 3, p. 250): short quote: "three-way handshake".
For TCP connection closing, remind students that the connection is full duplex. Each side closes its own sending direction with FIN=1, and the other side acknowledges that FIN. One side may close while the other briefly continues sending data.
Explain the FIN/ACK exchange as the teardown counterpart to setup. The goal is to inform the application that no more data will be sent and to clean up connection state in an orderly way.
Visible slide keywords: Closing a TCP connection, client, server each close their side of connection, send TCP segment with FIN bit = 1, respond to received FIN with ACK, on receiving FIN, ACK can be combined with own FIN, simultaneous FIN exchanges can be handled, Transport Layer: 3-, 29.
Quick question: does TCP close with a single message? No, because the two directions are closed separately with FIN and ACK exchanges.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.

## Slide 30: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality
Notes: Slide 30 - Principles of reliable data transfer
Book reference (Kurose & Ross, Chapter 3, p. 227): short quote: "TCP is said to be connection-oriented".
Use this closing roadmap slide to show that the connection-oriented TCP block is complete. At this point, students should be able to connect segment fields, sequence/ACK logic, timeout and fast retransmit, rwnd-based flow control, and the three-way handshake.
The next major topic is congestion control. Flow control looks at the receiver buffer, while congestion control looks at congestion in the network. Together, they shape TCP sender behavior.
Visible slide keywords: Chapter 3: roadmap, Transport-layer services, Multiplexing and demultiplexing, Connectionless transport: UDP, Principles of reliable data transfer, Connection-oriented transport: TCP, Principles of congestion control, TCP congestion control, Evolution of transport-layer functionality, Transport Layer: 3-, 30.
Final check: ask students to name TCP header fields used for reliability, flow control, and connection management.
Close the slide by connecting it to the next one: this mechanism is one part of the control information the transport layer adds so applications can communicate in a more organized and manageable way.