## Slide 1: Applied Sciences Faculty Management Information Systems
Dr. Yakup BAKIŞ
Notes: Last week, we talked about how the Internet works in general.
Today, we move one layer higher. We will begin to understand the Application Layer, which is the layer closest to the user.
When you open a website, send an email, or use Instagram, you are using the Application Layer.
This is the part of networking that you actually see and use every day.

## Slide 2: Chapter 1
Computer Networks and
the Internet
Notes: How many of you use the Internet every day? Probably all of you. But today, we will start learning how to build the web, not just use it. That is the difference between a user and an engineer. Users consume technology. Engineers understand and create technology.

## Slide 3: introduction
Chapter goal:
Get “feel,” “big picture,” introduction to terminology
  more depth, detail later in course
Approach:
  use Internet as example
Overview/roadmap:
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
History
Notes: The goal of this chapter is to give you a big picture. We are not going very deep today. We just want to understand the terminology and the general structure. Later in the course, we will go into much more detail. Today is about understanding the map. Later, we will explore each street.

## Slide 4: 1.1 What Is the Internet?
There are a couple of ways to answer this question.
First, we can describe the nuts and bolts of the Internet, that is, the basic hardware and software components that make up the Internet.
Second, we can describe the Internet in terms of a networking infrastructure that provides services to distributed applications.
Let’s begin with the nuts-and-bolts description, using Figure 1.1 to illustrate our discussion.
Notes: There are two main ways to define the Internet. First, we can describe its hardware and software components. This is what we call the nuts-and-bolts view. Second, we can describe the Internet as a service platform for applications. Today, we will start with the nuts-and-bolts view.

## Slide 5: The Internet: a “nuts and bolts” view
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Notes: The Internet connects billions of devices. These devices are called hosts or end systems. They run applications like web browsers, email, and streaming apps. These hosts are connected by communication links. Links can be fiber, copper, radio, or satellite. The devices that forward data are called packet switches. The most important packet switch is the router.

## Slide 6: 1.1.1 A Nuts-and-Bolts Description
Notes: The Internet is a computer network that interconnects billions of computing devices throughout the world.
The Internet is no longer just computers.
Increasingly, users connect to the Internet with smartphones and tablets—today, close to half of the world’s population are active mobile Internet users with the percentage expected to increase to 75% by 2025.
Furthermore, nontraditional Internet “things” such as TVs, gaming consoles, thermostats, home security systems, home appliances, watches eye glasses, cars, traffic control systems, and more are being connected to the Internet.
In Internet jargon, all of these devices are called hosts or end systems.
The Internet is becoming a network of smart devices.

## Slide 7: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force
Skype
WiFi
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Ethernet
HTTP
IP
4G
TCP
Streaming
video
ISP = Internet Service Provider
Internet = decentralized system
No central authority controls the whole Internet
Standardization enables global interoperability
Notes: The Internet is not a single network.
An ISP is an Internet Service Provider. For example, Turk Telekom or Vodafone or Superonline. But no single ISP covers the whole world. So ISPs must connect to each other ISPs.
They exchange traffic and share data. This connection between ISPs is called interconnected ISPs. That is why the Internet is called a network of networks.
Many independent networks are connected together to form one global system.
ISPs connect homes, companies, universities, and data centers. When you open a website, your ISP communicates with other ISPs to deliver the data to you.
Now, how do all these networks understand each other? The answer is: Protocols.
Protocols are everywhere in the Internet. They control how messages are sent and received. They define the format and the rules of communication.
For example: HTTP is used for the Web. TCP and IP are used for reliable data delivery. WiFi and 4G are used for wireless communication. Streaming protocols are used for video services.
Without protocols, devices could not communicate. It would be chaos.
But who defines these protocols? This is where Internet standards come into play. The Internet works not because it is controlled by one company, but because everyone follows the same rules.
Internet standards are written in documents called RFCs — Request for Comments. These standards are developed by an organization called the IETF — Internet Engineering Task Force.
Thanks to these standards, devices made by different companies can communicate with each other.

## Slide 8: 1.1.1 A Nuts-and-Bolts Description
In Internet jargon, all of these devices are called hosts or end systems.
End systems are connected together by a network of communication links and packet switches.
Different links can transmit data at different rates, with the transmission rate of a link measured in bits/second.
The resulting packages of information, known as packets, which are reassembled into the original data.
Packet switches come in many shapes and flavors, but the two most prominent types in today’s Internet are routers and link-layer switches.
a packet from the sending end system to the receiving end system is known as a route or path through the network.
    Packets are sent independently
    The Internet is a packet-switched network.
    The user does not see the complexity behind data transmission.
    This packet-switching architecture increases efficiency and allows multiple users to share the same network resources.
Notes: When data is sent through the Internet, it is not transmitted as one large file. Instead, it is divided into small pieces called packets.
Each packet contains not only a portion of the data, but also control information such as the source address and destination address. This additional information allows the network to deliver the packet to the correct destination.
These packets travel independently through the network. They pass through devices called routers and link-layer switches, which are collectively known as packet switches.
The sequence of communication links and packet switches that a packet follows from the sender to the receiver is called a route or path.
It is important to understand that different packets belonging to the same file may take different routes through the network. The Internet does not guarantee that all packets will follow the same path.
At the destination end system, all packets are collected and reassembled into the original data. If everything arrives correctly, the user sees the complete file without noticing this complex process.
End systems are connected together by a network of communication links and packet switches. These communication links are built from different types of physical media, such as coaxial cable, copper wire, optical fiber, and wireless radio spectrum.
Each communication link has a transmission rate, which is measured in bits per second. Some links are very fast, such as fiber-optic connections, while others may be slower, such as wireless connections.
Packet switches come in many forms, but the two most important types in today’s Internet are routers and link-layer switches.
Routers typically operate in the network core and make forwarding decisions based on IP addresses. Link-layer switches usually operate within local networks and forward data based on MAC addresses.
Together, communication links and packet switches form the infrastructure that allows data to move across the global Internet.

## Slide 9: The Internet: a “service” view
Infrastructure that provides services to applications:
  Web, streaming video, multimedia teleconferencing, email, games, e-commerce, social media, inter-connected appliances, …
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
HTTP
Skype
Streaming
video
provides programming interface to distributed applications:
  “hooks” allowing sending/receiving apps to “connect” to, use Internet transport service
  provides service options, analogous to postal service
1.1.2 A Services Description
This perspective helps us understand that the Internet is not just hardware
it is a programmable platform for distributed applications.
Notes: Another way to define the Internet is as a service platform. Instead of focusing on cables, routers, and hardware, we can think of the Internet as an infrastructure that provides services to applications.
These applications include the Web, email, video streaming, online games, video conferencing, social media, and many more.
The important point is this: The Internet itself does not run these applications. The applications run on end systems. The Internet simply provides the communication service between them.
So how do applications communicate over the Internet? They use something called a socket interface.
A socket is like a communication door between a program and the Internet. It allows a program to send and receive data using Internet transport services.
In this sense, the Internet is similar to a postal service. When you send a letter, you follow certain rules. You put the letter in an envelope, write the address, and drop it in a mailbox.
Similarly, applications must follow certain rules to send data across the Internet. The Internet provides different types of services, just like the postal service offers standard delivery, express delivery, and tracking options.
In the same way, the Internet offers different transport services, such as reliable delivery or faster but less reliable delivery.

## Slide 10: 1.1.3 What Is a Protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when message received, or other events
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on msg transmission, receipt
The Internet works because millions of devices agree to follow the same protocols. Protocols are the fundamental building blocks of all networked systems.
Notes: In the previous slide, we defined the Internet as a service platform. We said that applications use a socket interface to communicate.
But here is the key question: How does the Internet know what to do with the data sent through a socket?
The answer is: Protocols.
A protocol defines the rules of communication between network entities. It defines the format of messages. It defines the order of messages. And it defines what actions are taken when a message is sent or received.
In other words, protocols tell devices how to talk to each other.
Without protocols, communication would be chaos. Devices would send data in different formats, in random order, without understanding each other.
Just like humans follow social rules when speaking, computers follow protocols when communicating.
For example: When you say “What’s the time?”, there is an expected reply.
Similarly, in networking, when a client sends a request, the server must send a response in a specific format. The Internet works because millions of devices agree to follow the same protocols.
This is how applications, sockets, and the Internet infrastructure work together. Applications request services. Sockets provide the interface. Protocols define the communication rules.
And this is what makes the global Internet possible.

## Slide 11: What’s a protocol?
A human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Think about a human conversation. First, we say “Hi.” Then the other person replies. Then we ask a question. This is a protocol. Computers do the same thing. For example, a browser sends a TCP connection request. The server replies. Then the browser sends a GET request.
Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 12: A closer look at Internet structure 1.2 The Network Edge
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Notes: Now we move to a closer look at the Internet structure. We start with something called the network edge.
The network edge contains the hosts. In Internet terminology, hosts are also called end systems.
Hosts can be:
Clients
Servers
Clients request data. Servers provide data.
For example, when you open a website, your computer is the client. The web server in a data center is the server.
Today, many servers are located in large data centers around the world.

## Slide 13: A closer look at Internet structure 1.2 The Network Edge
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Notes: Now, how do these hosts connect to the Internet?
They use something called an access network.
Access networks connect end systems to the first router of the ISP.
These connections use physical media. Physical media can be:
Wired links
Wireless links
For example:
Fiber optic cables
Copper cables
WiFi
Cellular networks

## Slide 14: A closer look at Internet structure 1.2 The Network Edge
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Notes: After the network edge, we have the network core.
The network core is made of interconnected routers.
This is the part of the Internet that moves packets across long distances.
Remember: The Internet is called a network of networks because many networks are connected together through routers.

## Slide 15: 1.2.1-2 Access networks and physical media
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks (WiFi, 4G/5G)
What to look for:
transmission rate (bits per second) of access network?
shared or dedicated access among users?
Notes: Now the important question: How do end systems connect to the edge router?
There are three main types:
Residential access networks
Institutional access networks
Mobile access networks
When we evaluate an access network, we look at:
Transmission rate
Whether access is shared or dedicated
Transmission rate is measured in bits per second. And some networks are shared among many users, while others are dedicated per user.

## Slide 16: Access networks: cable-based access
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing (FDM): different channels transmitted in different frequency bands
1.2.1-2 Access networks and physical media
Notes: Cable Internet uses frequency division multiplexing, or FDM.
This means different signals use different frequency bands.
For example:
Some frequencies carry TV signals
Some frequencies carry Internet data
All of this travels over the same cable.

## Slide 17: Access networks: cable-based access
cable
modem
splitter
…
cable headend
data, TV transmitted at different
frequencies over shared cable
distribution network
HFC: hybrid fiber coax
  asymmetric: up to 40 Mbps – 1.2 Gbs downstream transmission rate, 30-100 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
cable modem
termination system
CMTS
ISP
1.2.1-2 Access networks and physical media
Notes: HFC stands for Hybrid Fiber Coax.
It uses fiber in the backbone and coaxial cable to homes.
It is asymmetric.
That means:
Download speed is higher
Upload speed is lower
Homes share the same cable network to the cable headend. So bandwidth is shared.

## Slide 18: Access networks: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  24-52 Mbps dedicated downstream transmission rate
  3.5-16 Mbps dedicated upstream transmission rate
DSL
modem
splitter
DSL access
multiplexer
1.2.1-2 Access networks and physical media
Notes: DSL stands for Digital Subscriber Line.
It uses existing telephone lines.
Voice and data use different frequencies.
The DSLAM at the central office separates voice and Internet data.
DSL usually provides dedicated access to each home.
Cable is shared. DSL is typically dedicated.

## Slide 19: Access networks: home networks
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
WiFi wireless access
point (54, 450 Mbps)
wireless
devices
often combined
in single box
1.2.1-2 Access networks and physical media
Notes: Inside your home, you usually have:
A modem
A router
A firewall
NAT
Ethernet
WiFi access point
Often, all of these are combined into one device.
How many of you have a WiFi router at home?

## Slide 20: Wireless access networks
Shared wireless access network connects end system to router
via base station aka “access point”
Wireless local area networks (WLANs)
  typically within or around building (~100 ft)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
to Internet
to Internet
Wide-area cellular access networks
  provided by mobile, cellular network operator (10’s km)
  10’s Mbps
  4G cellular networks (5G coming)
1.2.1-2 Access networks and physical media
Notes: Wireless networks connect devices to routers through access points.
WiFi works within buildings. Cellular networks cover wide areas.
WiFi is usually faster locally. Cellular networks provide mobility.

## Slide 21: Access networks: enterprise networks
companies, universities, etc.
  mix of wired, wireless link technologies, connecting a mix of switches and routers (we’ll cover differences shortly)
    Ethernet: wired access at 100Mbps, 1Gbps, 10Gbps
    WiFi: wireless access points at 11, 54, 450 Mbps
Ethernet
switch
institutional mail,
web servers
institutional router
Enterprise link to
ISP (Internet)
1.2.1-2 Access networks and physical media
Notes: Companies and universities use enterprise networks.
These networks combine:
Ethernet switches
Routers
WiFi access points
They connect many users and servers internally and then connect to an ISP.

## Slide 22: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=
1.2.1-2 Access networks and physical media
Notes: When a host sends data, it:
Takes the application message
Breaks it into packets
Sends each packet into the access network
If a packet has L bits and the transmission rate is R bits per second
The transmission delay is: L divided by R.
Transmission delay equals packet length divided by link rate.

## Slide 23: Links: physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet
1.2.1-2 Access networks and physical media
Notes: Physical links can be:
Guided media
Unguided media
Guided media includes:
Copper
Fiber
Coaxial cable
Unguided media includes:
Radio waves

## Slide 24: Links: physical media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise
1.2.1-2 Access networks and physical media
Notes: Coaxial cable has two copper conductors. It supports broadband transmission.
Fiber optic cable uses light pulses.
It provides:
Very high speed
Very low error rate
Long-distance transmission

## Slide 25: Links: physical media
Wireless radio
signal carried in electromagnetic spectrum
no physical “wire”
broadcast and “half-duplex” (sender to receiver)
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  up to 45 Mbps channels
Wireless LAN (WiFi)
  Up to 100’s Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10’s Mbps
satellite
  up to 45 Mbps per channel
  270 msec end-end delay
  geosynchronous versus low-earth-orbit
1.2.1-2 Access networks and physical media
Notes: Wireless radio signals travel through electromagnetic spectrum.
There is no physical wire.
But wireless is affected by:
Reflection
Obstacles
Interference
Satellite links have high delay because the signal travels very long distances.

## Slide 26: 1.3 The Network Core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Notes: Now we move from the network edge to the network core. The network core is the mesh of interconnected routers and links that connects all end systems.
The key idea here is packet switching. Hosts break application-layer messages into smaller pieces called packets. Then routers forward these packets from one router to the next, across links, until they reach the destination.
In packet switching, each packet is transmitted at the full link capacity on each link it uses.
So the core’s job is simple to say, but complex to do: move packets efficiently and reliably across the Internet.

## Slide 27: Packet-switching: store-and-forward
Transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
Store and forward: entire packet must arrive at router before it can be transmitted on next link
End-end delay: 2L/R (above), assuming zero propagation delay (more on delay shortly)
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec
1.3.1 Packet Switching
Notes: Let’s understand a very important concept: store-and-forward.
First, transmission delay: If a packet has length L bits and the link rate is R bits per second, the time to push the packet into the link is L divided by R seconds.
Store-and-forward means the router must receive the entire packet before it can send it on the next link.
In a simple one-router path, ignoring propagation delay, the end-to-end transmission delay becomes 2L/R: L/R to reach the router, and L/R to reach the destination.
The key message is: routers do not forward “half packets”—they typically wait for the full packet first.

## Slide 28: Packet-switching: queueing delay, loss
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for a period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
1.3.1 Packet Switching
Notes: Now we add a real-world effect: queueing.
Routers have output buffers, also called queues. If packets arrive faster than the link can send them, they must wait in the queue.
In this figure, hosts send data at high speed, but the outgoing link is slower. So packets build up in the queue.
If the buffer becomes full, packets are dropped. That is packet loss.
A good analogy is traffic: if cars arrive faster than the road can handle, a traffic jam forms; if the road is completely blocked, some cars must take another action.
So packet switching gives flexibility, but it can also create delay and loss when there is congestion.

## Slide 29: Two key network-core functions
Forwarding:
local action: move arriving packets from router’s input link to appropriate router output link
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
local forwarding table
local forwarding table
routing algorithm
1.3.1 Packet Switching
Notes: The network core has two key functions: forwarding and routing.
Forwarding is a local action inside one router. The router looks at the destination address in the packet header and sends the packet to the correct output link using a forwarding table.
Routing is a global action. It decides the end-to-end paths that packets take from source to destination. Routing algorithms compute these paths and help routers build their forwarding tables.
So in simple words: Routing chooses the road map; forwarding moves the packet at each intersection.

## Slide 30: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks
1.3.1 Packet Switching
Notes: Packet switching is the main idea of the Internet, but there is another approach called circuit switching.
In circuit switching, end-to-end resources are reserved for a call or session. This means a fixed part of the link capacity is dedicated to you for the whole communication.
The advantage is predictable performance. The disadvantage is inefficiency: if you are silent or not sending data, that reserved capacity is wasted.
Traditional telephone networks are classic examples of circuit switching.

## Slide 31: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
each call allocated its own band, can transmit at max rate of that narrow band
Time Division Multiplexing (TDM)
time divided into slots
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band, but only during its time slot(s)
1.3.2 Circuit Switching
Notes: Now we will briefly go deeper into circuit switching, mainly to compare it with packet switching. In circuit switching, the link resources can be divided in two common ways: FDM and TDM.
With FDM, the frequency spectrum is divided into bands. Each call gets its own band continuously.
With TDM, time is divided into repeating slots. Each call gets a time slot in each frame.
So FDM shares by frequency, and TDM shares by time.

## Slide 32: Packet switching versus circuit switching
Example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
packet switching allows more users to use network!
N
users
1 Gbps link
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
circuit-switching: 10 users
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
packet switching: with 35 users, probability > 10 active at same time is less than .0004 *
1.3.2 Circuit Switching
Notes: Here we see an important argument for packet switching.
In real life, many users are not active all the time. People send data in bursts: sometimes active, sometimes idle.
Packet switching can statistically support more users because it allocates capacity on demand.
The main idea to remember is: packet switching is efficient for bursty traffic, but it can also create congestion.

## Slide 33: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees traditionally used for audio/video applications
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?
1.3.2 Circuit Switching
Notes: So, is packet switching always better? Not always.
Packet switching is great because:
it shares resources efficiently
it is simpler, no call setup
But if the network becomes congested, we can get:
packet delay
packet loss
That is why networking needs protocols for:
reliable data transfer
congestion control
Later in the course, we will learn how TCP helps provide reliability and control congestion.